## Slide 1: Advanced Industrial Design Engineering
GRAP2575
Lecturers: Nick Johns & Rick Butcher

## Slide 2: Engineering for manufacture
Lean manufacturing
Design for disassembly and re-manufacture
Scalable, distributed and open-source modes of advanced and additive manufacturing
Mass-manufacture
Mass-customization
The social, cultural and environmental dimensions of product manufacturing and use will also be explored.

## Slide 3: Show and Tell
If you find any interesting videos, websites or articles relating to manufacturing, materials or processes please share them.
Email a link to your lecturer
Will be uploaded onto myRMIT

## Slide 4: Week #4 – Engineering Autopsy
Product Engineering Autopsy
Using the selected material maps (appendix - charts 1 to 6) categorise your materials/components based on the charts.
Document why specific materials were used in the product.
Identify whether alternative materials could have been used for specific components.
Task beyond class
Add info based on appendix charts into your autopsy report.
Collate assignment to myRMIT:
1 x stop motion video
1 x PDF or HTML document containing:
  High quality image of disassembled product
  Product/Component information – material type, manufacturing process, surface treatment, weight and dimensions
  Material properties - BOM
  Critical review of the product based on work undertaken thus far and design and technical elements of the product.
Read the prescribed Sustainable Design text(s).
To be uploaded onto myRMIT before the next class in week five.

## Slide 5: Indexing products by attributes

## Slide 6: Intentions in design
A single product may have more than one dominant intention, such as;
Market
  For public / private use…
  For women / elderly…
Economics
  Minimum cost
  Assembly
Sustainable
  Recycling / biodegradability
Performance
  Maximum Insulation

## Slide 7: Material Selection - Boundaries
Define the boundary conditions
Functions:
  Must it support a load?
  Must it contain a pressure?
  Must it transmit heat? Etc.

## Slide 8: Material Selection - Boundaries
Define the boundary conditions
Functions:
  Must it support a load?
  Must it contain a pressure?
  Must it transmit heat? etc.
Constraints:
  Are certain dimensions fixed?
  Must it carry the design loads without failure?
  Must it insulate or conduct?
  Can it function in a certain temperature range & in a given environment? Etc.

## Slide 9: Material Selection - Boundaries
Define the boundary conditions
Functions:
  Must it support a load?
  Must it contain a pressure?
  Must it transmit heat? etc.
Constraints:
  Are certain dimensions fixed?
  Must it carry the design loads without failure?
  Must it insulate or conduct?
  Can it function in a certain temperature range & in a given environment? etc.
Objectives:
  to make it as cheap as possible?
  to make it as light, or as safe as possible?
  the least environmental impact?

## Slide 10: Metals
Grand Arch II (1983).
Inge King
Powder coated steel, edition of 4 plus 1 artist's proof, 94.5 x 83.5 x 45 cm

## Slide 11: Metals
QUIESCENCE 2011.
Matthew Harding
Corten steel 160 x 110 cm dia, 85 x 60 cm dia Sculpture by the Sea 2011

## Slide 12: Metals
No 202 Metal construction.
Robert Klippel
Brazed and welded steel, found objects, 1966

## Slide 13: Metals
Jean Prouvé was once quoted saying: ‘never design anything that cannot be made.’

## Slide 14: Metals
Hard, malleable, plastic and highly controllable, metals are also very strong and extremely good conductors of electricity and heat. (Sea of valence electrons)

## Slide 15: Ceramics
Chilean studio Great Things to People (gt2P) has built a machine to generate pottery objects using an analogue version of parametric design.

## Slide 16: Ceramics
Very hard and strong, but lack flexibility making them brittle. Extremely resistant to high temperatures and chemicals. Ceramics are usually not good conductors of electricity or heat.

## Slide 17: Polymers
Growing up in the 20thC with new plastics, including the Raymond Loewy designed Gestetner Mimeograph machine and the flexible Mr. Gumby and his talking horse Pokey! (modeled by Art Clokey)
One of the reasons for Gumby’s green color is that it represents chlorophyll, which turns light into life.

## Slide 18: Poly-Mers
Mostly soft and not as strong as metals or ceramics. Polymers can be extremely flexible. Low density and viscous behavior under elevated temperatures are typical polymer traits. Polymers can be insulative to electricity.

## Slide 19: Pine cells
Composites can be engineered to combine more features than monolithic materials. However, this can create macro and / or micro stresses which impact upon the eco-system.

## Slide 20: Yellow Pine cells
Koch, P. 1972a. Utilization of the southern pines. I. The raw material. USDA Forest Service Agricultural Handbook No. 420. 733 pp.
Koch, P. 1972b. Utilization of the southern pines. II. The raw material. USDA Forest Service Agricultural Handbook No. 420. 926 pp

## Slide 21: Cellular material systems

## Slide 22: Control and the fold

## Slide 23: Material Selection - Free variables
Certain parameters can be adjusted in order to optimize the objective.
  Where the designer is free to vary dimensions that are not constrained by design requirements.
  Where the designer is free to choose the material for the component.
We refer to these as free variables.

## Slide 24: Manufacturing boundaries
Manufacturing processes can also play a role in constraining the selection.
The designer may be interested in a material that can be processed in a specific way (such as the processes in use in the available manufacturing plant) therefore limiting the choice of materials.

## Slide 25: Screen the attributes
Unbiased selection requires that all materials are considered to be candidates until shown to be otherwise.
Successful candidates must meet certain requirements or ‘attribute limits’.
Eliminate materials that cannot do the job.

## Slide 26: Rank by ‘Material Indices’
Rank materials that do the job best
A material index measures how well a candidate that has passed the screening steps can perform, and therefore meet the objective
For example:
  The best materials for buoyancy are those with the lowest density, .
  those best for thermal insulation the ones with the smallest values of the thermal conductivity, .

## Slide 27: Seek documentation
Typically descriptive, graphical or pictorial
  Case studies of previous uses of the material
  Details such as
    Corrosion behavior
    Availability
    Pricing
    Environmental impact
    Design Standards
  Such information is found in handbooks, suppliers’ data sheets, CD-based data sources and web sites.
  Documentation helps match
    Design requirements
    Material attributes

## Slide 28: Material Selection

## Slide 29: Flexibility
Looking for a light & stiff material? A chart of Young’s modulus (Elasticity) and density for materials guides the choice.
The chart was created using the CES EduPack 2007 software with the Level 2 database. Granta Design

## Slide 30: Flexibility
The index E/, describing the objective of stiffness at minimum weight, plotted on a chart. The best choices are materials with the greatest value of E/ that at the same time meet all other constraints. Granta Design

## Slide 31: Thermal properties
Looking for a material with low thermal expansion or expansion that matches another material? A chart of thermal conductivity and thermal expansion for materials is instructive.
The chart was created using the CES EduPack 2007 software with the Level 2 database. Granta Design

## Slide 32: Conducts heat & insulates
Need a material that conducts heat well but is an electrical insulator? A chart of thermal conductivity and electrical resistivity for materials may provide answers.
The chart was created using the CES EduPack 2007 software with the Level 2 database. Granta Design

## Slide 33: Family, Class & Member Profile

## Slide 34: Family, Class & Member Profile

## Slide 35: Shaping, Joining & Surface

## Slide 36: Shaping, Joining & Surface

## Slide 37: Shaping, Joining & Surface

## Slide 38: Intuition & perspective
The charts put material properties in perspective; For example;
Metals are 20 to 100 times stiffer than polymers and can conduct heat 100 times faster.

## Slide 39: Intuition & perspective
The charts put material properties in perspective; For example;
Metals are 20 to 100 times stiffer than polymers and conduct heat 100 times faster.
Elastomers have enormous expansion coefficients but are excellent electrical insulators.

## Slide 40: Intuition & perspective
The charts put material properties in perspective; For example;
Metals are 20 to 100 times stiffer than polymers and conduct heat 100 times faster.
Elastomers have enormous expansion coefficients but are excellent electrical insulators.
This “order of magnitude” familiarity is useful;
Much engineering design is intuitive.
Intuition is informed by just this sort of familiarity.

## Slide 41: Map your autopsy
Classify each component material as
  Family
  Class / Sub-class
  Member
  Profile
Classify each component process as
  Family
  Class / Sub-class
  Member
  Profile
Plus Aesthetic attributes & Perceptions of attributes

## Slide 42: Materials autopsy

## Slide 43: Process autopsy

## Slide 44: Homework
Submit assignment 1
For details, see http://www.studiobutcher.com/sb-aide-week-4.html